## Slide 1
Public Bus Stop Accessibility and Service Gaps Across Chennai
Exploratory analysis of a bus stop audit
210 stops audited | 85 variables

## Slide 2
Problem, Objectives and Method
Exploratory analysis, not causal inference
Objectives
Pedestrian and wheelchair movement
Bus-to-kerb boarding conditions
Shelter roof, shade, seating, capacity
Encroachment, drainage and safety
Stop name and route information
Land-use context and priorities
Method
Data loading, quality checks, whitespace and date cleanup, duplicate removal, missing-value review, derived indicators, frequency analysis and charts.
Pedestrian access score
Counts Yes for: space behind shelter, space between shelter and road, continuous footpath movement (0 to 3).

## Slide 3
Pedestrian Access Is Weak
Share of audited stops meeting each condition (%)
Chart: 
| Space behind shelter | Space between shelter and road | Pass without stepping on road | All three conditions
% of stops | 25.2 | 28.6 | 26.2 | 12.9
12.9%
of stops satisfy all three pedestrian-access conditions
Fewer than 3 in 10 stops allow pedestrians or wheelchair users to move freely.

## Slide 4
Boarding, Encroachment and Drainage
Physical conditions around the stop
20.0%
flush boarding position (under 30 cm)
47.6%
partially encroached
11.4%
heavily encroached
27.1%
water-logging or drainage issues
Four in five stops have a boarding gap of 30 cm or more, and about 59% are encroached to some degree.

## Slide 5
Lighting and Passenger Information
Safety and information gaps
17.6%
inadequate or no lighting
34.8%
no route information displayed
27.6%
no clearly displayed stop name
Over a third of stops give passengers no route information at all.

## Slide 6
Recommendations
Priority actions for a targeted improvement program
Pedestrian access
Footpath continuity, clear movement space, accessible approaches
Boarding gaps
Better kerb and platform design; align bus stopping positions
Encroachment
Manage parked vehicles, vendors and construction material
Lighting
Upgrade lighting at unsafe or poorly lit stops
Information
Clear, current route info and legible stop names
Drainage
Fix water-logging around affected stops
Shelters
Review capacity, shade, seating and roof condition

## Slide 7
Limitations and Conclusion
Limitations
Audit sample may not cover every Chennai stop
Some fields are missing
Responses are partly subjective
Results should not be generalized city-wide
Conclusion
Gaps are concentrated in pedestrian movement, boarding distance, encroachment, lighting and passenger information. The derived indicators can help prioritize stops for infrastructure and service upgrades.